## Slide 1: Synthetic Data Generation for Navigation in GPS-Denied Environment
Shunguang Wu
06/25/2022
- An outline for APL ASPIRE Students in 2022 Summer

## Slide 2: Background: Computational Platform and Sensors
System on Chip (SoC) Computer
VectorNav (at 50-100Hz)
GPS (lat, lon, height)
Inertial Measurement Unit (IMU)
-acc: acceleration in body-fixed coordinates
-gyro: delta angle rotation around three axis
Magnetic field of the earth
Baro: flight height based on air pressure
Other
Camera (at 30 or 60Hz)
Measure platform velocity based on pixel change between two image frames
Range Sensor (at 50Hz)
Measure range from camera to scene
(image from web)

## Slide 3: What we shall do in this summer
Create a rigid body platform, and put the three sensors on it
Design some flight paths
Generate synthetic measurement data for VectorNav
Flight the rigid body platform along the paths
Verify and visualizing the generated data
Literature review: navigation in GPS denied environment
(week 1, work together)
(week 2,3, work together)
(week 2-6)
Continue development and prepare a IEEE-STEM conference paper
(Deadline: at the end of December )
(Fall semester, optional)
Learn Basic Matlab
Learn Basic git and open gitHub account
Generate synthetic measurement data from Camera & range sensor.
Verify and visualizing the generated data
Student A
Student B

## Slide 4: Literature review: Navigation in GPS denied environment
What kind of platforms and sensors the community use?
Why do we need it?
(No math, just high level common sense kind of concept/understanding)
What kind of measurements these sensors providing?
Why people using synthetic data in R&D?

## Slide 5: Matlab
Basic data type, vector, and 2d-matrix operations
Should be already installed in your machine
figure, plot(), and plot3()

## Slide 6: Create a rigid body platform
Hints
Qs: what kind of shape we should choose, what is the simplest one with minimum parameters and good/close enough to the reality?
There should have a body-fixed coordinate system on this platform, each sensor should have a (x, y, z) coordinate on it.
Hint: Math to describe the rigid-body?
Hint: Matlab visualization

## Slide 7: Design flight paths
Global coordinate reference (earth fixed)
Some paths may considering
(lat, lon, height)
ECEF
ENU or NED
Matlab function to transfer from one to another
A 2D line (with fixed height)
A 2D circle (with fixed height)
Oval / ellipse (with fixed height)
etc.
Coding practice: generate a path and plot it
(image from web)

## Slide 8: VectorNav synthetic measurements
Problem1: Given a rigid body in flight (global measurement), how to generate its local measurement (IMU and Gyro)?
Problem2: Given the local measurement (IMU and Gyro), how to recover its global flight path?
1 and 2 can be used to verify the correctness of each other
Repeat the above steps by adding Gaussian noise?

## Slide 9: VectorNav synthetic measurements
struct Nav{
  uint64_t fn{ 0 }; //sample index
  uint64_t time_us{ 0 }; //sample time in macro second, 1 sec = 1e6 us
  uint8_t gpsNumSats{ 0 }; //num of satellite
  vec3f gpsMeasPosLla{}; //[deg,deg,m]
  vec3f gpsMeasVelNed{}; //[deg,deg,m]
  vec3f gpsMeasPosU{ 0 }; //NED unsertainty (m)
  vec3f gpsMeasVelU{ 0 }; //NED Vel uncertainty (m/s)
  vec3f mag[3] //Gauss:compensated magnetic measurement
  float pressure{ 0 }; //kPa: compensated pressure measurement
  uint32_t deltaTime_us{ 0 }; //delta time in macro sec
  vec3f deltaTheta{}; //gyro deg
  vec3f deltaVel{}; //imu m/sec
};

## Slide 10: Camera – synthetic measurements (approach 1)
Problem: Given (lat, lon, height), camera parameters (focal length, imgW, imgH), and view angle (look down) can we retrieve a google earth image?
Basic Image format (bmp, jpg, png) and its data structure in Matlab.
Load an image from file, manipulate, display, and save it with different format
Study if there any open source to solve this problem?
Or
What is the math behind this problem?
(image from web)

## Slide 11: Camera – synthetic measurements (approach 2)
Problem: given platform flight velocity in NED, camera parameters (focal length, imgW, imgH, view angle) can we retrieve optical flow?
what is optical flow (without math)?
pixel flow: Image based (dx, dy)
from pixel flow to angular flow
from angular flow to global velocity
Part 1: learn
Part 2: solve the original problem by inversing part 1
(image from web)
(If we solved the problem in approach 1, we do not need to go approach 2)
(I will give more slides to detail these steps)

## Slide 12: Camera – flow data structure
struct FlwSample{
  uint64_t img_fn{0}; //image frame number
  uint64_t time_us{0}; //image frame time in macro second
  int32_t flow_quality{ 0 };//-1 marked not publishing the flow to EKF
  uint32_t dt_us{ 0 }; //time interval between two frames in macro second
  float flow_x_pix{0}; //pixels in image coordinate: top left(0,0), x-right, y-down
  float flow_y_pix{0}; //pixels in image coordinate
  float flow_x_rad{0}; //radius flow
  float flow_y_rad{0}; //radius flow
  float integrated_x_gyro_rad{0};
  float integrated_y_gyro_rad{0};
  float integrated_z_gyro_rad{0};
  float vel_x_mps{0}; //m/s, Flow in x-sensor direction, angular-speed compensated
  float vel_y_mps{0}; //m/s, Flow in y-sensor direction, angular-speed compensated
  float range_meas{0};
};

## Slide 13: Administration
Team meeting Friday: 4 - 5pm
Source code and document at gitHub
Present what you did in the past week and what you will do in coming week
OK no show, but need to notify me earlier
Use APL official Email for communications, ask me if you have any questions
Create you account at GitHub, and email me your account url
Will invite you to the project
Work on APL provided computer.
Box for sharing data files

## Slide 15: Navigation in GPS Denied Environment
(students figure it out in literature review)